To configure your switches:
Configure all access ports to allow non-tagged PXE booting connections from each slave node to the Fuel Master node. This network is referred to as the Fuel network.
By default, the Fuel Master node uses the eth0 interface to serve PXE requests on this network, but this can be changed during installation of the Fuel Master node.
If you use the eth0 interface for PXE requests, you must set the switch port for eth0 on the Fuel Master node to access mode.
- We recommend that you use the eth0 interfaces of all other nodes for PXE booting as well. Corresponding ports must also be in access mode.
- Taking into account that this is the network for PXE booting, do not mix this L2 segment with any other network segments. Fuel runs a DHCP server, and, if there is another DHCP on the same L2 network segment, both the company's infrastructure and Fuel's are unable to function properly.
- You must also configure each of the switch's ports connected to nodes as an "STP Edge port" (or a "spanning-tree port fast trunk", according to Cisco terminology). If you do not do that, DHCP timeout issues may occur.

Network	VLAN	IP RANGE
Admin (Fuel)	1 - No VLAN	10.20.0.0/24
Public	100	172.16.0.0/24
Storage	101	192.168.0.0/24
Management	102	192.168.1.0/24
Private	103	192.168.3.0/24
Internal	104	192.168.111.0/24

qmlk
Switch	Public			Private
Port	1	2-3	24	1	2-7	23	24
Link Type	TRUNK	GENERAL	GENERAL	TRUNK	GENERAL	GENERAL	GENERAL
Egress Rule	TAG	UNTAG	UNTAG	TAG	UNTAG	UNTAG	UNTAG
PVID	1	100	1	1	1,101-104	1	1

Switch	Admin
Port	1	2-6	23
Link Type	TRUNK	GENERAL	GENERAL
Egress Rule	TAG	UNTAG	UNTAG
PVID	1	1	1

Switch	Public
Port	1	2-6	23
Link Type	TRUNK	GENERAL	GENERAL
Egress Rule	TAG	TAG	UNTAG
PVID	1	1,100,101,102	1,100

Switch	Private
Port	1	2-6
Link Type	TRUNK	GENERAL
Egress Rule	TAG	TAG
PVID	1	103,104

### Networking Option 2: Self-service networks¶
The self-service networks option augments the provider networks option with layer-3 (routing) services that enable self-service networks using overlay segmentation methods such as VXLAN. Essentially, it routes virtual networks to physical networks using NAT. Additionally, this option provides the foundation for advanced services such as LBaaS and FWaaS.